## Slide 1: Unit 1.5 - Network Topologies, protocols and layers Lesson 3

## Slide 2: Engagement Activity
What is Internet anyway?
https://www.youtube.com/watch?v=95-yZ-31j9A

## Slide 3: Big Picture
Networks transfer and receive a lot of data
In one minute on the Internet: 640TB data transferred. This lesson considers how such a huge amount of data is sent to ensure that it arrives at the correct computer

## Slide 4: Learning Objectives
Know what layers are and their role
Be able to explain the role of each layer
Understand the concept of Packet Switching

## Slide 5: Key Words
Layers
Packet Switching

## Slide 6: Packet Switching
Imagine that you have a large LEGO model to post through a letter box but, it does not fit.
What could you do?
What if you could take the model apart and then post it through the letter box and then reassembly it?
This is packet switching

## Slide 7: Packet Switching
Now image you want to email a photo, first it is broken down into small packets of data
Each packet is then given a header which contains the IP address of the network and device that it is being sent to.
It also contains the IP address of the network that it was sent from

## Slide 8: Packet Switching
The header also contains the packet number as well as the total number of packets, for example packet 4 of 60, packet 45 of 60.
When the packets arrive at the destination this information is used to reassemble the data.
Packets can be lost so sometimes the computer request the packet to be sent again, if a packet never arrives then it is deleted by the router.

## Slide 9: An example Packet
http://optimus5.com/index.php?page=search/images&search=tcp+ip+packet&type=images&startpage=4

## Slide 10: Activity 1 – Understanding a Packet
Research one of the parts of the packets that you do not know. Explain it to another students.

## Slide 11: Video
https://www.youtube.com/watch?v=WwyJGzZmBe8

## Slide 12: Activity 2
Play packet switching game
  Resources from http://code-it.co.uk/netintsearch

## Slide 13: Layers
As a packet is prepared the data travels through layers where protocols manage it, adding or removing extra information as required.
https://www.youtube.com/watch?v=zyL1Fud1Z1c

## Slide 14: Key Words Recap
Layers
Packet Switching

## Slide 15: Plenary
Create a short film or story board explaining the concept of either:
  Packet switching
  Layers
Create a quiz on the topics covered in this lesson

## Slide 16
OCR Resources: the small print OCR’s resources are provided to support the teaching of OCR specifications, but in no way constitute an endorsed teaching method that is required by the Board, and the decision to use them lies with the individual teacher. Whilst every effort is made to ensure the accuracy of the content, OCR cannot be held responsible for any errors or omissions within these resources. © OCR 2016 - This resource may be freely copied and distributed, as long as the OCR logo and this message remain intact and OCR is acknowledged as the originator of this work.
OCR acknowledges the use of the following content: n/a
Please get in touch if you want to discuss the accessibility of resources we offer to support delivery of our qualifications: resources.feedback@ocr.org.uk